INT 10 - VESA SuperVGA BIOS - GET SuperVGA 
INFORMATION

Classification: video
	AX = 4F00h
 	ES:DI -> 256-byte buffer for SuperVGA 
information (see below)
Returns:
AL = 4Fh function supported
 	AH = status
 	    00h successful
 	    01h failed

Description:
determine whether VESA BIOS extensions are present and the 
capabilities supported by the display adapter
See also: AX=4F01h AX=7F00h 
Index:	installation check;VESA
 
Format of SuperVGA information:

Offset	Size	Description
  00h  4 BYTEs	signature ('VESA')
  04h	WORD	VESA version number
  06h	DWORD	pointer to OEM name
 		"761295520" for ATI
  0Ah  4 BYTEs	capabilities
  0Eh	DWORD	pointer to list of supported VESA 
and OEM video modes
 		(list of words terminated with 
FFFFh)
  12h 238 BYTEs	reserved

----------------------------
INT 10 - VESA SuperVGA BIOS - GET SuperVGA 
MODE INFORMATION

Classification: video
	AX = 4F01h
 	CX = SuperVGA video mode
 	ES:DI -> 256-byte buffer mode 
information (see below)
Returns:
AL = 4Fh function supported
 	AH = status
 	    00h successful
 	    01h failed

Description:
determine the attributes of the specified video mode
See also: AX=4F00h AX=4F02h 

Format of mode information:
Offset	Size	Description
  00h	WORD	mode attributes
 		bit 0: mode supported
 		bit 1: optional information 
available
 		bit 2: BIOS output supported
 		bit 3: set if color, clear if 
monochrome
 		bit 4: set if graphics mode, 
clear if text mode
  02h	BYTE	window A attributes
 		bit 0: exists
 		bit 1: readable
 		bit 2: writable
 		bits 3-7 reserved
  03h	BYTE	window B attributes (as for 
window A)
  04h	WORD	window granularity in K
  06h	WORD	window size in K
  08h	WORD	start segment of window A
  0Ah	WORD	start segment of window B
  0Ch	DWORD	-> FAR window positioning 
function (equivalent to AX=4F05h)
  10h	WORD	bytes per scan line

---remainder is optional for VESA modes in 
v1.0/1.1, needed for OEM modes---
  12h	WORD	width in pixels
  14h	WORD	height in pixels
  16h	BYTE	width of character cell in pixels
  17h	BYTE	height of character cell in pixels
  18h	BYTE	number of memory planes
  19h	BYTE	number of bits per pixel
  1Ah	BYTE	number of banks
  1Bh	BYTE	memory model type (see below)
  1Ch	BYTE	size of bank in K
  1Dh	BYTE	number of image pages
  1Eh	BYTE	reserved (0)

---VBE v1.2+---
  1Fh	BYTE	red mask size
  20h	BYTE	red field position
  21h	BYTE	green mask size
  22h	BYTE	green field size
  23h	BYTE	blue mask size
  24h	BYTE	blue field size
  25h	BYTE	reserved mask size
  26h	BYTE	reserved mask position
  27h	BYTE	direct color mode info
  28h	BYTE	reserved (0)
 
Values for memory model type:
  00h text
  01h CGA graphics
  02h HGC graphics
  03h 16-color (EGA) graphics
  04h packed pixel graphics
  05h "sequ 256" (non-chain 4) graphics
  06h direct color (HiColor, 24-bit color)
  07h YUV (luminance-chrominance)
  08h-0Fh reserved for VESA
  10h-FFh OEM memory models

-----------------------------------------
INT 10 - VESA SuperVGA BIOS - SET SuperVGA 
VIDEO MODE

Classification: video
	AX = 4F02h
 	BX = mode
 		bit 15 set means don't clear 
video memory
Returns:
AL = 4Fh function supported
 	AH = status
 	    00h successful
 	    01h failed
See also: AX=4F01h AX=4F03h 

Values for VESA video mode:
  00h-FFh OEM video modes (see AH=00h)
  100h	640x400x256
  101h	640x480x256
  102h	800x600x16
  103h	800x600x256
  104h	1024x768x16
  105h	1024x768x256
  106h	1280x1024x16
  107h	1280x1024x256
  108h	80x60 text
  109h	132x25 text
  10Ah	132x43 text
  10Bh	132x50 text
  10Ch	132x60 text

---VBE v1.2---
  10Dh	320x200x32K
  10Eh	320x200x64K
  10Fh	320x200x16M
  110h	640x480x32K
  111h	640x480x64K
  112h	640x480x16M
  113h	800x600x32K
  114h	800x600x64K
  115h	800x600x16M
  116h	1024x768x32K
  117h	1024x768x64K
  118h	1024x768x16M
  119h	1280x1024x32K
  11Ah	1280x1024x64K
  11Bh	1280x1024x16M
Index:	video modes
 
Values for S3 OEM video mode:
  201h	640x480x256
  202h	800x600x16
  203h	800x600x256
  204h	1024x768x16
  205h	1024x768x256
  206h	1280x960x16
  208h	1280x1024x16
  301h	640x480x32K

Index:	video modes

-----------------------------------------
INT 10 - VESA SuperVGA BIOS - 
SAVE/RESTORE SuperVGA VIDEO STATE

Classification: video
	AX = 4F04h
 	DL = subfunction
 	    00h get state buffer size
 		Return: BX = number of 64-byte 
blocks needed
 	    01h save video states
 		ES:BX -> buffer
 	    02h restore video states
 		ES:BX -> buffer
 	CX = flags for states to save/restore
 	    bit 0: video hardware state
 	    bit 1: video BIOS data state
 	    bit 2: video DAC state
 	    bit 3: SuperVGA state
Returns:
AL = 4Fh function supported
 	AH = status
 	    00h successful
 	    01h failed

INT 10 - VESA SuperVGA BIOS - CPU VIDEO MEMORY CONTROL

Classification: video
	AX = 4F05h
 	BH = subfunction
 	    00h select video memory window
 		DX = window address in video memory (in granularity units)
 	    01h get video memory window
 		Return: DX = window address in video memory (in gran. units)
 	BL = window number
 	    00h window A
 	    01h window B
Returns:
AL = 4Fh function supported
 	AH = status
 	    00h successful
 	    01h failed